## Slide 1: IMU based GIS mapping of Electrical Grid
Team : Gyoku Hou Unit

## Slide 2: Problem Statement
Mapping the electrical network is a long and tedious process, but in reality is quite simple.
The GPS coordinates and certain electrical data like Inter Connection Transformer, 100MVA , 400/132/33 kV and so on for other elements in the grid is required to be entered into a simple text doc. Entering data is done by hand in sheets and then manually entered in desktop.
From experience working with conventional GPS devices, collecting and plotting 4 points took about an hour.

## Slide 3: Limited to a small network
The process mentioned above is quite simply impractical for large transmission and convoluted distribution networks.
To make the process more concise and faster, a simple device create the text file as well as get the GPS coordinates using a reference point and a magnetometer is the solution, I propose.

## Slide 4: Assumptions and pre-requisites
One reference point whose coordinates are known (la1, lo1).
Radius of the earth (R) = 6317km
The distance between the reference point and destination point should be entered into the device manually (d).
All values entered in the formula are to be expressed in radians.
The above are required for calculation purposes.

## Slide 5: Heading
Heading is the direction in which a person moves with respect to the North pole.
The output of the magnetometer is used to calculate the person’s heading.
The heading (φ) here is needed to determine the coordinates of the next point.
These are calculated using the following formulae.

## Slide 6: Formula
Φ = atan(mag.y, mag.x)
la2 = asin(sin(la1)*cos(Ad)+cos(la1)*sin(Ad)*cos(φ))
lo2 = (lo1)+(atan2(sin(φ)*sin(Ad)*cos(la1),cos(Ad)-sin(la1)*sin(la2)));
Ad = d/R

## Slide 7: The Device
The device comprises of a simple keypad to enter details like type of element and electrical rating.
An SD card reader to make a text file and have all the data entered in a particular format.
A magnetometer and MC to calculate the heading and coordinates.
A simple display to complete the device.

## Slide 8: Future Scope
The next phase once the files are created correctly, is to add connectivity to the device to allow one to send the files either via email or share it via cloud to enable a seamless and quick transfer of data, if required.

## Slide 9
Thank You